## Slide 1: Rietveld Structure Refinement of Protein Powder Diffraction Data using GSAS
Jon Wright
ESRF, Grenoble, France

## Slide 2: Plan…
This is a users perspective
Cover the protein specific aspects (assuming knowledge of Rietveld and some familiarity with GSAS)
Reading in data/model and setting up a refinement
Reading in restraints files, setting parameters for Marquardt damping & band matrix for least squares
Use of spdbv for viewing structure, maps, modifying/fixing side chains, Ramachandran plots

## Slide 3: A users perspective!
GSAS – General Structure Analysis System, Larson and Von Dreele
July 6,1999 – First “protein” version became available
Any errors, omissions and fundamental misunderstandings presented here should be attributed to me, and not GSAS or it’s authors!
Notes: Make clear that JPW is giving this talk only because no one else seemed to be available!
JPW has not contributed to software development, only benefited by being able to use it.
Note the picture from the cover of the manual… you should read it before getting started!

## Slide 4: Protein structure from powder data??
Fundamental differences to small molecule crystallography
  Lots of geometric constraints
  only ,  and sidechain conformations which are unknown
Low resolution crystallography
R
C




C
C
R. B. Von Dreele, J. Appl. Cryst. (1999). 32, 1084-1089
“…refinement of the 1261-atom protein metmyoglobin was achieved by combining 5338 stereochemical restraints with a 4648-step (dmin = 3.3 Å) ”
[3783 x,y,z co-ordinates from only 4648 datapoints!]
  Restraints provide short range info, powder data for longer range
Notes: We are not refining a structure at atomic resolution (individual atom positions are not important), but looking for how the protein chain folds and packs in the unit cell. Blobs of amino acid rather that atoms at 3 Angstrom resolution.
It is now 2003 – four years later. Software is stable, reliable, works well.
Real point is that a lot of stereochemistry is known about proteins - bonds, angles, chiral "volumes", torsions (single & coupled chi1/chi2 ones), planes, etc. All subject to use as constraints & provide a lot of short distance info for structure. Powder data gives precision long distance info.

## Slide 5: Setting up a refinement…
Need a dataset and a PDB file containing a model
Insert phase and flag as “macromolecule”
Insert data as normal
You might try a LeBail fit to get good peakshape and cell parameters
Tip!
For starting a LeBail fit only use the low angle portion of the pattern
(severe overlaps)
Notes: In practice I never bother to do LeBails in GSAS – generally more trouble than it’s worth to get a LeBail fit to behave!

## Slide 6: Example used here…
Myoglobin (horse)
Crystallised by salting out with ammonium sulphate
Data collected at BM16, ESRF
λ = 0.4135Å
See Jeremy Cockcroft (FA 5 - MS 7, Wednesday pm) for other examples at this conference
Notes: Note the short wavelength

## Slide 7
Inserting the atoms is trivial, when the structure is available in a PDB file !
The PDB file, unit cell and dataset must “match”
Notes: Whether to copy HOH, H and disordered depends on the quality of the PDB file and how close you think that single crystal was to your sample.
It is probably worth comparing the results with and without the various contributions.
MUST ENSURE the structure gets to be read in “correctly” and that the cell/matrix works out right.
This is a metmyoglobin problem as there are two "conventions" about making the Cartesian coordinates used in PDB files - you ought to mention this earlier.

## Slide 8: Choose the right cell
Indexing produced two (equivalent) unit cells, which correspond to two choices for a monoclinic set of axes, both close to an orthorhombic cell.
a = 64.20502 a = 63.5722
b = 28.92236 b = 28.9320
c = 35.85339 c = 35.8645
beta = 107.1616 beta = 105.386
Chi^2 = 21.28 Chi^2 = 122.92
Fits using deposited single crystal structure factors (works better than comparing to the model !!)
Notes: Fits were produced in some version of prodd (could also use fullprof, or any program which reads an hkl for doing lebail type fits).
Do one cycle at a time and keep supplying the same hkl file to have fixed intensities (or hack the program).
Missing peaks at low angles were not recorded in the single crystal experiment, or at least are missing from the deposited structure factors.
A looong time was spent when I got started as I had the wrong cell. It is like trying to smash the square peg in the round hole.

## Slide 9: Solvent scattering…
Tends to build up electron density in regions which are far from any atoms
Fills in the void space in the structure with smooth density
Works “surprisingly well”
Parameters have some physical meaning
Expedt: L F S
Notes: Should perhaps have plotted the real space over a different range.
Recheck the gnuplot script before getting to Durban!!
A=6.63 isn't really "physical" since form factors can't be negative. I always get A<6.0 (usually between 5 & 6).

## Slide 10
Solvent scattering
Fits with and without solvent contribution
“Babinet’s principle” gives modified atomic scattering factors:
Here A=6.63e- and U=1.18Å2 (so carbon effectively has no electrons at low angles!)











2
2
2
0
sin
8
exp
λ
θ
U
π
A
f
f
Notes: Makes a very large impact on the fit

## Slide 11: Setting up restraints:
GSAS provides macros containing standard amino acid geometries
Macromolecule phases identify amino acids for working out restraints
Treat non-amino acid groups manually (eg heme, ligands etc)
Use the macro files in $GSAS/macros/, then
“expedt, L S” for soft restraints
a @r angles.mac
x d @r bonds.mac
x k @r chiral.mac
x r @r rama.mac
x t @r torsion.mac
x p @r planes.mac
…takes a few minutes, depending on the speed of the computer (and typist)

## Slide 12: Get a good fit BEFORE refining atom positions!
Time spent ensuring the peak shape, unit cell and background are good will pay off later
Try at least one cycle with restraints present but positions fixed to see how well the geometry matches
The restraints should be well fitted at the start if you have a sensible model
Notes: Sadly I never got a PDB file for the myoglobin which looks much better than that (eugh) – wrong cell choice looks quite similar. Maybe the SX refinement is dodgy?
Jeremy Cockcroft has some Lysozyme and RnaseA data which did much better for the starting model (virtually did not need refinement!)

## Slide 13: Cross your fingers….
And let all the co-ordinates go!
Don’t refine UISO, just set it to 0.3.
Apply some Marquardt damping (stability)
Set max atom shift to 0.25-0.5Å
Set the matrix bandwidth (speed)
  try to be wide enough to preserve restraints
Damping is the restraint/observation that the current model is correct
Multiplies diagonal of LSQ matrix by Marquardt factor
set
to zero
Notes: Width ought to include at least one, and ideally two or three amino acids
Some things – like heme to chain can still get lost
Full matrix just takes a lot longer
Might mention setting the max atom shift to 0.25-0.5A to keep things under control. Also mention uselessness of refining UISO. I set it to 0.3 (that's a B=23) & leave it alone. The band works because it follows along the protein main chain & the protein atoms are ordered in GSAS (& PDB files) along the chain. Probably wouldn't if the atoms weren't ordered.

## Slide 14: Did it fly to pieces?
Use the “GSAS2PDB” program to output your structure
Use some more specialised protein software to inspect your refined structure
Notes: Inevitably it’s the part restrained manually which falls to bits, and not the amino acids with GSAS’s excellent macros!!
(I had to delete the angle and planar restraints to make this picture… no, really I did)
Another useful tool is PROCHECK - tells about bad chi angles, etc. It along with SPDBV can be used to fix (i.e. "mutate") side chains to get more reasonable conformations. May be a little guidence from Fourier plots (2fdf, etc. are useful)

## Slide 15: PROCHECK Laskowski R A, MacArthur M W, Moss D S & Thornton J M (1993). “PROCHECK: a program to check the stereochemical quality of protein structures.” J. Appl. Cryst., 26, 283-291. http://www.biochem.ucl.ac.uk/~roman/procheck/procheck.html
Detailed geometry checks for ensuring a sensible structure
Highlights areas needing attention

## Slide 16: spdbv : an ideal partner to GSAS
FORPLOT writes fourier maps which can be read here
Reads and writes pdb files
Allows side chains to be “repaired”
freeware from http://www.expasy.org/spdbv

## Slide 17
Structure energy calculations in spdbv complement the restraints used in GSAS to highlight any problematic areas
(GROMOS, inside spdbv ignores some intermolecular non-bonded contacts which GSAS includes, so they don’t exactly agree)

## Slide 18
Rwp
10.18%
Rwp
7.65%

## Slide 19
Rwp ~ 7.65 %
Rwp ~ 10.18 %
~10 cycles
takes around 2 minutes per cycle (1.6 GHz P4)
Not even time for lunch!

## Slide 20
(another 60 cycles later….) Rwp 4.53%
Further improvement is doubtless possible, but the structure essentially reproduces the data and still gives about the same folds as the original. Geometry is still (just) acceptable for the checks in spdbv.
Notes: Fits to data which Jeremy Cockcroft will present later in the week did much better.
The myoglobin is further from the structure in the PDB file, presumably due to different crystallisation conditions (more aggressive salting out to get microcrystals instead of large single crystals might mean there are some other sulphates in there…)

## Slide 21: A (biased) omit map
Fix the x,y,z of everything
Set the occupancy of the interesting region to zero
Run a (zero cycle) genles + fourier
FORPLOT for difference map
  o option to make a DN6
Read into spdbv along with pdb file to visualise

## Slide 22: Summary
Setting up restraints for a “standard” amino acid chain is automated
Interaction with PX software is facilitated by PDB and DN6 map file formats
New features can be applied elsewhere
  Solvent scattering – zeolite channels?
  Marquardt damping – difficult structures
  DN6 maps for any fouriers
  PDB files for easy H-bonding checks in mercury (visualisation software from CCDC)
  Macro files for any restrained refinements

## Slide 23: Don’t forget…
Flag the phase as a macromolecule
  p p m 1 d
Put some solvent scattering in
  l f s
Add and check the restraints
Use a band matrix and some damping
  l l b 50 (or more)
  l l d 1.5
Bob Von Dreele has deposited data and structures for refinements in IUCr journals – you can practise on these
ccp14 tutorial at: http://www.ccp14.ac.uk/solution/gsas/peak_and_proteins.html

## Slide 24: Acknowledgement
Bob Von Dreele
  Giving away his program
  Lots of useful advice and encouragement
ESRF
  my generous employer!